## Slide 1
7F COMBUSTION SECTION
DISASSEMBLY – VR TRAINING
PROOF OF CONCEPT
PRESENTED BY XALTER, INC.
PRESENTED TO GE VERNOVA
DISASSEMBLY SCOPE · SCENES 1–4 · SINGLE COMBUSTION CAN
SCOPE: Assumes shutdown, LOTO, and zero-energy verification already complete · PoC target: 10–15 min headset experience

## Slide 2
MEETING GOAL & VALIDATION SCOPE
OBJECTIVE
Validate step-by-step procedural accuracy and safety considerations for the disassembly of a single GE 7F combustion can.
Roy (Roy) will review each scene, correct inaccuracies, and confirm safety gates — then annotate the slide deck offline for the next session.
Goal: get GEV executives in the headset for 10–15 minutes to prove VR/XR is superior to traditional R.
SCOPE — PROOF OF CONCEPT
1. Scene 1: Tool & Consumable Selection (Digital Picklist)
2. Scene 2: Forward Can, Fuel Nozzle & Liner Cap Removal
3. Scene 3: Crossfire Tubes, Liner & Flow Sleeve Removal
4. Scene 4: Transition Piece Removal
Out of Scope: Shutdown, LOTO, upper casing removal, full reassembly
ASSUMPTION · Machine is shut down, LOTO complete, zero-energy verified, and upper turbine casing pre-removed. Mechanics are entering the combustion section.

## Slide 3
SCENE 1
Digital Picklist: Tool Selection
GOAL · Learner selects correct tools from the outage unit staging area. Wrong selections trigger a coaching gate.
MECHANICAL TOOLS
Learner must select all of the following:
• 1/2-inch impact wrench
• 3/4-inch 12-point socket
• 3/16-inch Allen wrench
• 5/16-inch Allen wrench
• Dead blow hammer
• Torque wrench
(rated 125 ft-lb)
RIGGING EQUIPMENT
Heavy-lift gear required — several components exceed 1,000 lbs.
• Crane / overhead lift
• Rigging straps / slings
Rigging is basic field skill — mechanics determine their own setup. VR models rigging at approximate form factor; not engineered-precise.
CONSUMABLES
New gaskets required for:
• Fuel nozzle flange connection
• Forward-to-aft can joint
Anti-seize available for specific screws (assembly goes together mostly dry).
Note: No barcode scanning in field — VR mechanic TBD per GEV feedback.
VALIDATE WITH ROY: Are all tools listed correct and complete? Are there additional consumables? Confirm gasket locations.

## Slide 4
SCENE 2
Forward Can, Fuel Nozzle & Liner Cap Removal
GOAL · Remove the first major assembly — forward can, fuel nozzle, and liner cap come off as a single combined unit.
FLANGE BOLT REMOVAL
Use 1/2-inch impact wrench + 3/4-inch 12-point socket.
Approx. 24–36 bolts on the forward can flange (exact count TBD — GEV to confirm).
Efficiency mechanic: learner performs 2–3 bolts manually, then simulation auto-completes remainder.
COMBINED ASSEMBLY LIFT
Once bolts are removed, forward can + fuel nozzle + liner cap slide off as a SINGLE combined assembly.
Weight: approx. 1,000 lbs
Learner must rig crane/lift before extraction. Assembly lifts out via overhead crane — VR crane model directionally accurate, not engineered-precise.
⚠ SAFETY GATE — GASKET
Gasket must be visually confirmed present on fuel nozzle flange before assembly is cleared.
A second gasket sits at the forward-to-aft can joint — both must be identified and staged as replaced parts before the scene advances.
VALIDATE WITH ROY: Confirm bolt count (24 vs. 36). Confirm crane lift is correct method. Are there additional disconnect steps before the assembly slides off?

## Slide 5
SCENE 3 — PART 1 OF 2
Crossfire Tubes: Retaining Fork Removal & Pullback
GOAL · Crossfire tubes MUST be cleared before the combustion liner can be removed — hard sequence gate.
CROSSFIRE TUBE FUNCTION
Tubes connect all 14 combustion chambers, carrying fire from spark plugs (in 2 of 14 chambers) to the rest of the unit.
Each aft can contains a crossfire tube port on the flow sleeve; tubes are a male and female two-piece assembly.
REMOVAL SEQUENCE
1. Remove the retaining fork (fork-style clip) that holds the crossfire tube in place
2. Pull the male and female tube sections back to clear the liner extraction path
Tubes are NOT fully removed — they are retracted back into their ports.
⚠ SAFETY GATE — SEQUENCE LOCK
Attempting to pull the combustion liner before both crossfire tubes are retracted:
Hard block — reflects real mechanical constraint (liner physically cannot clear the crossfire tube ports).
VALIDATE WITH ROY: Is fork removal correct terminology? Are both inner and outer crossfire tube sections retracted, or just pulled back? Confirm sequence gate is accurate.

## Slide 6
SCENE 3 — PART 2 OF 2
Combustion Liner & Flow Sleeve Removal
GOAL · Liner is extracted from the flow sleeve; flow sleeve is then pulled from the aft can.
LINER EXTRACTION
Remove 3 L-shaped indexing brackets using 3/16" Allen screws.
Brackets are attached to the liner and index into notches on the flow sleeve (aligning crossfire tube holes, spark plug holes, etc.).
Liner slides out forward — weight approx. 75 lbs, rigged via crane.
Liner: REPLACED. Has white ceramic thermal barrier coating.
FLOW SLEEVE REMOVAL
Once liner is extracted, the flow sleeve is pulled from the aft can.
Flow sleeve: REUSED — not replaced. No refurbishment step by mechanics.
Weight approx. 75 lbs — crane assist. The liner rides inside the flow sleeve; flow sleeve directs compressor airflow around liner for cooling.
X-RAY / TRANSPARENCY VIEW
Recommended VR mechanic: toggle a transparency view before extraction to visualize:
• How liner seats inside flow sleeve
• How flow sleeve seats inside aft can
• Spatial relationship to the transition piece
Roy confirmed: this is useful for learners building spatial mental model.
VALIDATE WITH ROY: Are 3/16" Allen screws correct for the L-brackets? Confirm liner vs. flow sleeve replacement/reuse decision. Is crane required for both, or can liner be manually extracted?

## Slide 7
SCENE 4
Transition Piece Removal
GOAL · Most technically detailed step — aft bracket bolts, bear claws, bullhorn disengage, and crane lift out the top.
COMPONENT OVERVIEW
The transition piece (TP) connects the combustion section to the first-stage turbine nozzle.
Forward (round) end sits in the Bullhorn Bracket.
Aft (rectangular) end bolts to the first-stage nozzle bracket at top of unit.
Has ceramic thermal barrier coating inside — REPLACED every CI.
Weight: approx. 150 lbs.
REMOVAL SEQUENCE
1. Go to aft bracket (top of unit) — 2 bolts into first-stage nozzle
2. Release Bear Claws — bend back the lock tabs that prevent bolt spin-out
3. Remove the 2 aft bolts
4. Slide the TP forward to disengage from the Bullhorn Bracket
5. Lift the TP out through the top of the unit via crane
Torque value (reassembly): 125 ft-lb
⚠ KEY GATES
Bear Claw Gate:
Learner must bend lock tabs back before attempting to spin bolts — attempting to remove bolts with bear claws locked triggers an error.
Slide Direction Gate:
TP must slide FORWARD to disengage from bullhorn bracket — attempting to lift before disengaging triggers a geometry warning.
Lift Path Gate:
TP exits through the TOP of the unit only.
VALIDATE WITH ROY: Confirm bolt count (2 at aft bracket). Are bear claws bent by hand or a tool? Confirm 125 ft-lb torque applies to this specific bracket. Confirm TP exits top only.

## Slide 8
REASSEMBLY — OUT OF PoC SCOPE (PLACEHOLDER)
Reassembly is reverse-order of disassembly with the following confirmed exceptions:
TRANSITION PIECE SEAL GAP MEASUREMENT
After bolting TP to first-stage nozzle, mechanic goes inside and measures seal engagement. Minimum: 1/8-inch engagement required. Side seals also slide down between adjacent TPs.
BEAR CLAWS — LOCK-IN
After bolts are torqued to 125 ft-lb, bear claw lock tabs are bent back over bolts to prevent spin-out.
GASKETS — NEW EVERY TIME
New gaskets installed at fuel nozzle flange and forward-to-aft can joint before reassembly.
ANTI-SEIZE — LIMITED USE
Anti-seize applied to specific screws only (not a full lubrication step). Assembly otherwise goes together dry.
NOTE · Full reassembly will be added to scope if XALTER and GE Vernova proceed beyond the PoC. This slide is a reference placeholder only.

## Slide 9
PARTS DISPOSITION: REPLACED vs. REUSED
COMPONENT | DISPOSITION | NOTES
Forward Can + Fuel Nozzle + Liner Cap | REPLACED | Come off as one combined assembly (~1,000 lbs, crane)
Combustion Liner (inner piece) | REPLACED | White ceramic TBC coating; ~75 lbs, crane out
Flow Sleeve (outer piece) | REUSED | Not refurbished — simply removed, inspected, reinstalled
Transition Piece | REPLACED | Ceramic TBC on inside; ~150 lbs; exits out top via crane
Gaskets (×2) | REPLACED | Fuel nozzle flange + forward-to-aft can joint
Crossfire Tubes | RETRACTED ONLY | Not removed — pulled back to allow liner extraction, then reseated
VALIDATE WITH Roy · Confirm all part dispositions. Are there any additional consumables or parts replaced at every CI that are not listed here?

## Slide 10
VR MECHANICS & SAFETY GATE SUMMARY
X-RAY / TRANSPARENCY VIEW
Toggle-on view to see liner inside flow sleeve, flow sleeve inside aft can, and spatial relationship to the TP before any extraction step. Roy confirmed: useful for learner spatial orientation.
SAFETY GATES — SEQUENCE LOCKS
1. Crossfire tubes must be retracted before liner can move
2. Bear claws must be released before TP bolts can spin
3. TP must slide forward before lift
4. Crane must be rigged before heavy assemblies can be moved
EFFICIENCY MECHANIC — BOLT SKIP
For repetitive bolt tasks (e.g., 24–36 flange bolts):
Learner performs 2–3 manually → simulation auto-completes remainder.
Keeps PoC engagement high without 30-min session time.
COACHING INTERVENTIONS
Wrong sequence → error message + reset to last valid state
Incorrect tool selection → coaching card explains correct choice
Missed gasket / bear claw → pop-up warning before scene advances
All interventions non-punitive for PoC — educational tone.
XALTER, INC. · CONFIDENTIAL · GE VERNOVA SCOPING SESSION · 7F COMBUSTION INSPECTION VR TRAINING PROTOTYPE

## Slide 11
POC SCOPE — WHAT WE'RE BUILDING & WHY
WHAT THE PoC DEMONSTRATES
VR/XR is superior to other modalities for complex industrial disassembly procedures. VR/XR may not replace instructor-led and/or CBT training, but it’s more real-world experiential with higher retention rates and more scalable than many other modalities.
Key proof points:
• Step-by-step procedural immersion
• Physics-based part interactions
• Safety gate enforcement without risk
• Scalable to all 14 combustion chambers
• Repeatable, consistent training delivery
Target audience for demo: GEV leadership (Jim and Cal)
SCOPE DECISIONS FROM THIS MEETING
IN — Disassembly only (Scenes 1–4)
IN — Efficiency bolt skip mechanic
IN — X-ray spatial view
IN — Rigging (form-accurate, not engineered-precise)
OUT — Shutdown / LOTO / casing removal
OUT — Full reassembly
OUT — Borescope inspection (done pre-outage by others)
Target headset time: 10–15 min
NEXT STEP · Roy / Linda to annotate deck with corrections by the end of this week and provide photos/video of rigging, crossfire tubes, L-brackets, and combustion liner. Schedule follow-up session next week.

## Slide 12
OPEN DISCUSSION
Technical Validation with Roy · Alpha Build Spec Lock
The following require Roy’s expert input before XALTER begins Alpha build.
BOLT COUNT & SEQUENCE
Exact count on the forward can flange (24 or 36+). Does a specific cross-pattern bolt removal sequence matter, or is it within range?
TORQUE VALUE — 125 FT-LB
Is 125 ft-lb correct specifically for the TP aft bracket bolts? Are there other torque-critical fasteners in Scenes 1–4?
COMMON FIELD ERRORS
What are the most frequent mistakes mechanics make during disassembly? Which should become coaching triggers in the VR?
PHOTOS / VIDEO NEEDED
GEV to provide: rigging equipment, crossfire tube retainers/forks, L-bracket indexing tabs, and combustion liner. Video preferred.
XALTER, INC. · CONFIDENTIAL · GE VERNOVA SCOPING SESSION · 7F COMBUSTION INSPECTION VR TRAINING PROTOTYPE